## Slide 1: Computer instruction set

## Slide 2
Outline
  Instruction
  Op-Code Encoding
  Encoding Techniques
    Block-Code Technique
    Expanding Op-Code Technique
    Huffman Encoding
  Addressing Modes
  Instruction Types

## Slide 3
An instruction manipulates the stored data, and a sequence of instructions constitutes a program. In general, an instruction has two components:
  Op-Code field
  Operand/Address Field (s)
The Op-Code field specifies how data is to be manipulated. The data items may reside within a CPU register or in the main memory. The purpose of the address field is to indicate the data address.
ADD R1, R2
Op-Code Field Address Fields

## Slide 4
The operand field may have the following formats:
  1) zero-address
  2) one-address
  3) two-address
  4) three-address
The total number of instructions and the types and formats of the operands determine the length of an instruction.

## Slide 5
The shorter the instruction, the faster the time that it can be fetched and decoded.
Shorter instructions are better than longer ones:
  (i) take up less space in memory
  (ii) transferred to the CPU faster
A machine with 2^N instructions must require at least N-bit to encode all the op-codes.

## Slide 6: Op-Code Encoding
A processor can execute an instruction only if it is represented as a binary sequence. A unique binary pattern must be assigned to each op-code. This process is known as op-code encoding. An example of op-code encoding using 3-bit block code is shown in the following table:
Op-Code | Binary Pattern
LDA | 000
STA | 001
ADD | 010
AND | 011
CMA | 100
INCA | 101
JMP | 110
HLT | 111

## Slide 7: Op-Code Encoding Techniques
Different Op-Code encoding techniques are:
  Block-code technique
  Expanding op-code technique
  Huffman Encoding

## Slide 8: Block-Code Technique - To each of the 2K instructions a unique binary bit pattern of length K is assigned. - A K-to-2K decoder can then be used to decode all the instructions. For example,
3-to-8
decoder
3-bit Op-code
instruction 0
instruction 1
instruction 2
instruction 3
instruction 4
instruction 5
instruction 6
instruction 7

## Slide 9
Expanding op-code technique
  Consider an 4+12 bit instruction with a 4-bit op-code and three 4-bit addresses.
  It can at most encode 16 three-address instructions.
  If there are only 15 such three-address instructions, then one of the unused op-code can be used to expand to two-address, one-address or zero address instructions.
  Again, this expanded op-code can encode at most 16 two-address instructions. And if there are less than 16 such instructions, we can expand the op-code further
Op-code
Address 1
Address 2
Address 3
1 1 1 1
Op-code
Address 1
Address 2
1 1 1 1
1 1 1 1
Op-code
Address 1
1 1 1 1
1 1 1 1
1 1 1 1
Op-code

## Slide 10: Huffman Encoding
  Given the probability of occurrences of each instruction, it is possible to encode all the instructions with minimal number of bits, and with the following property:
Fewer bits are used for most frequently used instructions and more for the least frequently used ones.
1
1/4
1/2
1/8
1/8
1/4
1/2
1/16
1/16
1/16
1/16
1/8
1/8
1/4
1/4
LOAD
STO
SHIFT
NOT
JUMP
HALT
AND
ADD
1
1
0
0
1
0
1
0
1
0
1
0
1
0
11
10
011
010
0011
0010
0001
0000

## Slide 11: Op-Code Encoding, Huffman Codes
Huffman encoding algorithm:
  Initialize the leaf nodes each with a probability of an instruction. All nodes are unmarked.
  Find the two unmarked nodes with the smallest values and mark them. Add a new unmarked node with a value equal to the sum of the chosen two.
  Repeat step (2) until all nodes have been marked except the last one, which has a value of 1.
  The encoding for each instruction is found by tracing the path from the unmarked node (the root) to that instruction.
may mark branches arbitrarily with 0, 1

## Slide 12: Op-Code Encoding, Huffman Codes (Cont.)
Advantage:
  minimal number of bits
Disadvantage:
  must decode instructions bit-by-bit, (can be slow).
  to decode, must have a logical representation of the encoded tree, and follow branches as we decipher bits
  Fact is, most decoding is done in parallel
    Gives a speed advantage

## Slide 13: Addressing modes
Inherent
  an op-code indicates the address of its operand CLI ; clear the interrupt flag
Immediate
  an instruction contains or immediately precedes its operand value ADD #250, R1 % R1 := R1 + 250;
Absolute/Direct
  an instruction contains the memory address of its operand ADD 250, R1 % R1 := R1 + *(250);
Register
  an instruction contains the register address of its operand ADD R2, R1 % R1 := R1 + R2;

## Slide 14: Addressing modes (cont.)
Register Indirect
  the register address in an instruction specifies the address of its operand ADD @R2, @R1 % *R1 := *R1 + *R2;
Auto-decrement or Auto-increment
  The contents of the register is automatically decremented or incremented before or after the execution of the instruction
  MOV (R2)+, R1 % R1 := *(R2); R2 := R2 + k;
  MOV -(R2), R1 % R2 := R2 - k; R1 := *(R2);

## Slide 15: Addressing modes (cont.)
Indexed
  an offset is added to a register to give the address of the operand MOV 2(R2), R1 % R1 := R2[2];
Base-register
  a displacement is added to an implicit or explicit base register to give the address of the operand
Relative
  same as base-register mode except that the instruction pointer is used as the base register

## Slide 16: Addressing modes (cont.)
Indirect addressing mode in general also applies to absolute addresses, not just register addresses; the absolute address is a pointer to the operand.
The offset added to an index register may be as large as the entire address space. On the other hand, the displacement added to a base register is generally much smaller than the entire address space.
The automatic modification (i.e., auto-increment or auto-decrement) to an index register is called auto-indexing.
Relative addresses have the advantage that the code is position-independent.

## Slide 17: Instruction Types
Instructions, of most modern computers, may be classified into the following five groups:
  Data transfer
    MOV, LOAD
  Arithmetic
    ADD, SUB, DIV, MUL
  Logical
    AND, OR, NOT, SHIFT, ROTATE
  System-control
    Test-And-Set
  I/O
    Separate I/O space input/output

## Slide 18: Instruction Types (cont.)
Program-control may be classified into the following four groups:
  Unconditional branch
    BRB NEXT % branch to the label NEXT
  Conditional branch
    SOBGTR R5, LOOP % repeat until R5=0
    ADBLEQ R5, R6, LOOP % repeat until R5>R6
  Subroutine call
    CALL SUB % push PC; branch to SUB
    RET % pop PC
  Interrupt-handling
    TRAP % generate an internal interrupt

## Slide 19: Instruction Types (cont.)
Typical branch instructions
  test the value of some flags called conditions.
  Certain instructions cause these flags to be set automatically.
linkage registers
  Used in implementing a subroutine.
  Typically include the instruction pointer and stack pointer..
The parameters passed between the caller and the called subroutine are to be established by programming conventions.
  Very few computers support parameter-passing mechanisms in the hardware.
An external interrupt may be regarded as a hardware generated subroutine call
  Can happen asynchronously.
  When it occurs, the current state of the computation must be saved either by
    the hardware automatically
    or by a program (interrupt-service routine) control.