## Slide 1: Registers

## Slide 2
Outline
  Registers
  Benefits of Registers
  Basic Register
  Shift Register
  Bidirectional Shift Register with Parallel Load

## Slide 3: Registers
Registers are common sequential devices.
  They’re a good example of sequential analysis and design.
  They are also frequently used in building larger sequential circuits.
Registers hold larger quantities of data than individual flip-flops.
  Registers are central to the design of modern processors.
  There are many different kinds of registers

## Slide 4: Benefits of registers
Flip-flops are limited because they can store only one bit.
  Two flip-flops are used for two-bit counters.
  Most computers work with integers and single-precision floating-point numbers that are 32-bits long.
A register is an extension of a flip-flop that can store multiple bits.
Registers are commonly used as temporary storage in a processor.
  They are faster and more convenient than main memory.
  More registers can help speed up complex calculations.

## Slide 5: A basic register
Basic registers are easy to build. We can store multiple bits just by putting a bunch of flip-flops together!
A 4-bit register is shown on the right, and its internal implementation is below.
  This register uses D flip-flops
  it’s easy to store data without worrying about flip-flop input equations.
  All the flip-flops share a common CLK and CLR signal.

## Slide 6
Figure: A 4-bit basic Register

## Slide 7: Shift register
A shift register “shifts” its output once every clock cycle.
SI is an input that supplies a new bit to shift “into” the register.
For example, if on some positive clock edge we have: SI = 1 Q0-Q3 = 0110
then the next state will be: Q0-Q3 = 1011
The current Q3 (0 in this example) will be lost on the next cycle.
Q0(t+1) = SI
Q1(t+1) = Q0(t)
Q2(t+1) = Q1(t)
Q3(t+1) = Q2(t)

## Slide 8: Bidirectional shift register with parallel load
A bidirectional shift register is one in which the data can be shifted either left or right. It can be implemented by using gate logic that enables the transfer of a data bit from one stage to the next stage to the right or to the left, depending on the level of a control line.

## Slide 9: Bidirectional shift register with parallel load (cont.)
S1 | S0 | Register Operation
0 | 0 | No change (Hold)
0 | 1 | Shift Left (down)
1 | 0 | Shift Right (up)
1 | 1 | Parallel Load
Parallel load
DOWN
UP
HOLD

## Slide 10
Figure: Bidirectional Shift Register with Parallel Load