## Slide 1: Register Transfer and microoperations

## Slide 2
Outline
  Register Transfer
  Bus and Memory Transfers
  Arithmetic Microoperations
  Logic Microoperations
  Shift Microoperations
  Arithmetic Logic Shift Unit (ALU)

## Slide 3: Register Transfer
Information transfer from one register to another is described by a replacement operator: R2 ← R1
This statement denotes a transfer of the content of register R1 into register R2
The transfer happens in one clock cycle
The content of the R1 (source) does not change
The content of the R2 (destination) will be lost and replaced by the new data transferred from R1
The circuits are available from the outputs of the source register to the inputs of the destination register, and that the destination register has a parallel load capability

## Slide 4: Register Transfer (cont.)
Conditional transfer occurs only under a control condition
Representation of a (conditional) transfer P: R2 ← R1
A binary condition (P equals to 0 or 1) determines when the transfer occurs
The content of R1 is transferred into R2 only if P is 1

## Slide 5: Register Transfer (cont.)
n
Clock
R1
R2
Control Circuit
Hardware implementation of a controlled transfer: P: R2 ← R1
Block diagram:
Load
P

## Slide 6: Bus and Memory Transfers
Paths must be provided to transfer information from one register to another
A Common Bus System is a scheme for transferring information between registers in a multiple-register configuration
A bus: set of common lines, one for each bit of a register, through which binary information is transferred one at a time
Control signals determine which register is selected by the bus during each particular register transfer

## Slide 7: Bus and Memory Transfers (cont.)
3 2 1 0
Register D
D3 D2 D1 D0
3 2 1 0
Register C
C3 C2 C1 C0
3 2 1 0
Register B
B3 B2 B1 B0
3 2 1 0
Register A
A3 A2 A1 A0
D3 C3 B3 A3
S0
S1
MUX3
3 2 1 0
D2 C2 B2 A2
S0
S1
MUX2
3 2 1 0
D1 C1 B1 A1
S0
S1
MUX1
3 2 1 0
D0 C0 B0 A0
S0
S1
MUX0
3 2 1 0
4-Line Common Bus
Register A
Register B
Register C
Register D
Bus lines

## Slide 8: Arithmetic Microoperations
The microoperations most often encountered in digital computers are classified into four categories:
  Register transfer microoperations
  Arithmetic microoperations (on numeric data stored in the registers)
  Logic microoperations (bit manipulations on non-numeric data)
  Shift microoperations

## Slide 9: Arithmetic Microoperations (cont.)
The basic arithmetic microoperations are: addition, subtraction, increment, decrement, and shift
Addition Microoperation:
R3 ←R1+R2
Subtraction Microoperation:
R3 ←R1-R2
or : R3 ←R1+R2+1
1’s complement

## Slide 10: Arithmetic Microoperations (cont.)
One’s Complement Microoperation:
R2 ←R2
Two’s Complement Microoperation:
R2 ←R2+1
Increment Microoperation:
R2 ←R2+1
Decrement Microoperation:
R2 ←R2-1

## Slide 11: Arithmetic Microoperations (cont.)
Binary Adder:
Figure: 4-bit binary adder (Connection of FAs)
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4

## Slide 12: Arithmetic Microoperations (cont.)
Binary Adder-Subtractor
Figure: 4-bit Adder-Subtractor
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4
M

## Slide 13: Arithmetic Microoperations (cont.)
Binary Adder-Subtractor (cont.)
When M=0 the circuit is an adder and when M=1 the circuit becomes a subtractor. Each Exclusive-OR gate receives input M and one of the inputs of B. When M=0, we have B 0=B. The full adders receive the value of B, the input carry is 0, and the circuit performs A plus B. When M=1, we have B 1= B´ and C0 = 1. the B inputs are all complemented and a 1 is added through the input carry. The circuit performs the operation A plus the 2’s complement of B. for unsigned numbers, the result is A-B provided that there is no overflow.

## Slide 14: Arithmetic Microoperations (cont.)
Binary Adder-Subtractor (cont.)
For unsigned numbers, this gives A – B if A≥B or the 2’s complement of (B – A) if A < B
(example: 3 – 5 = -2= 1110)
For signed numbers, the result is A – B provided that there is no overflow.
(example : -3 – 5= -8)
1101
1011 +
1000
C3
C4
V =
1, if overflow
0, if no overflow
Overflow detector for signed numbers

## Slide 15: Arithmetic Microoperations (cont.)
Binary Incrementer
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
S0
S1
S2
S3
C4
1
A0
A1
A2
A3
4-bit Binary Incrementer
Binary Incrementer can also be implemented using a counter
A binary decrementer can be implemented by adding 1111 to the desired register each time!

## Slide 16: Arithmetic Microoperations (cont.)
Arithmetic Circuit
This circuit performs seven distinct arithmetic operations and the basic component of it is the parallel adder
The output of the binary adder is calculated from the following arithmetic sum:
    D = A + Y + Cin

## Slide 17: Arithmetic Microoperations (cont.)
Arithmetic Circuit (cont.)
Figure: 4-bit Arithmetic Circuit

## Slide 18: Arithmetic Microoperations (cont.)
Arithmetic Circuit (cont.)
Arithmetic Circuit Function Table

## Slide 19: Logic Microoperations
Hardware Implementation
The hardware implementation of logic microoperations requires that logic gates be inserted for each bit or pair of bits in the registers to perform the required logic function
Most computers use only four (AND, OR, XOR, and NOT) from which all others can be derived.

## Slide 20: Logic Microoperations (cont.)
Hardware Implementation (cont.)
S1
S0
0
1
2
3
4×1 MUX
Ei
Ai
Bi
S1 | S0 | Output | Operation
0 | 0 | E = A  B | XOR
0 | 1 | E = A  B | OR
1 | 0 | E = A  B | AND
1 | 1 | E = A | Complement
One stage logic circuit

## Slide 21: Shift Microoperations
Used for serial transfer of data
Also used in conjunction with arithmetic, logic, and other data-processing operations
The contents of the register can be shifted to the left or to the right
As being shifted, the first flip-flop receives its binary information from the serial input
Three types of shift: Logical, Circular, and Arithmetic

## Slide 22: Shift Microoperations
Figure: 4-bit Combinational Circuit Shifter

## Slide 23: Arithmetic Logic Shift Unit
Instead of having individual registers performing the microoperations directly, computer systems employ a number of storage registers connected to a common operational unit called an Arithmetic Logic Unit (ALU)

## Slide 24: Arithmetic Logic Shift Unit (cont.)
0
1
2
3
S3
S2
S1
S0
Bi
Ai
Ai+1
Ai-1
Select
4×1 MUX
Ci
Ci+1
One stage of Arithmetic Circuit
One stage of Logic Circuit
Di
Ei
Fi
shr
shl
Figure: One stage of ALU