## Slide 1: Signed Magnitude data

## Slide 2: Eight Conditions for Signed-Magnitude Addition/Subtraction
Operation | ADD Magnitudes | SUBTRACT Magnitudes |  | 
 |  | A > B | A < B | A = B
(+A) + (+B) | + (A + B) |  |  | 
(+A) + (-B) |  | + (A – B ) | - (B – A ) | + (A – B )
(-A) + (+B) |  | - (A – B ) | + (B – A ) | + (A – B )
(-A) + (-B) | - ( A + B) |  |  | 
(+A) - (+B) |  | + (A – B ) | - (B – A ) | + (A – B )
(+A) - (-B) | + (A + B) |  |  | 
(-A) - (+B) | - ( A + B) |  |  | 
(-A) - (-B) |  | - (A – B ) | + (B – A ) | + (A – B )

## Slide 3: Flowchart of Addition and Subtraction with Signed-Magnitude Data
Ar = B – A
Ars = Bs
Start Subtraction
Start Addition
Bs = Bs′
As = Bs
Ar = A + B
Ars = As
A > B
Ar = A – B
Ars = As
A = B
Ar = 0
Ars = 0
Done

## Slide 4: Summary of Addition and Subtraction with Signed-Magnitude Data
The signs use an exclusive OR gate where if the output is 0, then the signs are the same.
Hence, add the magnitudes of the same signed numbers. If the sum is an overflow, then a carry is stored in E where E = 1 and transferred to the flip-flop AVF, add-overflow.
Otherwise, the signs are opposite and subtraction is initiated and stored in A.
No overflow can occur with subtraction so the AVF is cleared.
If E = 1, then A > B.
However, if A = 0, then A = B and the sign is made positive.
If E = 0, then A < B and sign for A is complemented.

## Slide 5: Addition and Subtraction with Signed-Magnitude Data Hardware Design
A register
AVF
E
Bs
As
B register
Complementer
Parallel Adder
S
Load Sum
M
Mode Control
Input Carry
Output Carry